## Slide 1: Dynamic Generation of Modular Industrial Plant Visualizations
Weekly Meeting 14
Miguel Romero Karam

## Slide 2: P&ID Viewer - Dashboard

## Slide 3: Sapient Boardlet Weekly Sprint 14

## Slide 4: Boardlet Design Updates & Fixes
Implemented progress bar for vertex placement algorithm (can change to any function with iteration)
Fixed responsive layout of buttons when wrapped (narrow mobile screens)
1) on start
2) in progress
3) done
desktop
mobile

## Slide 5: Data Bindings Overview
IDs of current values (primary key of p_values_current) stored in prj_prc_pro_flows under rate_value
Why are there only current values for flows ???
Only nodes with process variables have entry in p_values_current ???
Concept (getDataBindings):
  Fetch IDs under rate_value along with query for pidConnections – done
  For each ID: fetch and join p_values_config and p_values_current – done
  Construct a sapientBind object for each rate_value depending on value type
ToDo:
  Define data types: each data type (bool/int/float/string…) will have own sapientBind object for Example:
boolean (sets fillColor)
int (sets label) – concept because currently only bools
OR

## Slide 6: Queries for Current Values Overview: Data Map
p_values_current
id [PK] : Int
value_bool : Int
value_num : Double
value_str : String
value_date : Timestamp
time_stamp : Timestamp
last_archive_id : Int
last_update : Timestamp
…
p_values_config
id [PK] : Int
connection : Int
value_type : Int
value_format : Int
value_symbol: String
name_0: String
name_1: String
…
p_value_types
id [PK] : Int
name_0 : String
name_1 : String
description_0 : String
description_1 : String
…
prj_prc_visu_vertices
id [PK] : Int
is_instrument : Boolean
node : Int
shape_name : String
pid_label : String
pid_function : String
pid_number : String
l_nodes
id [PK] : Int
parent : Int
short_name : String
name_0 : String
description_0 : String
name_1 : String
description_1 : String
node_level : Int
node_type : Int
attr_jsonb : Jsonb
isaLevel : String
modelId : Int
valPrefix : String
standingData: Array
opcUALevel : Int
opcUANamespaceName : String
opcUAAddressPrefix : String
permissions : Int
…
prj_prc_pro_flows
id [PK] : Int
node0 : Int
node1 : Int
port0 : Int
port1 : Int
is_continuous : Boolean
product : Int
rate_value : Int
flow_type : String
copies
p_value_relations
id [PK] : Int
node: Int
value: Int
attr_jsonb : Jsonb
…

## Slide 7: Database Queries Nodes Query - Problem
SQL- Query:
Complex SQL Query with LEFT JOIN not possible with getRecords options
Workaround with javascript:
  2 distinct queries
  Left Join Function in javascript on common attribute.
l_nodes
LEFT JOIN
ON tree.id = vertex.node
Wanted Query Data
visu_vertices
prj_prc_visu_vertices
id [PK] : Int
is_instrument : Boolean
node : Int
shape_name : String
pid_label : String
pid_function : String
pid_number : String
l_nodes
id [PK] : Int
parent : Int
short_name : String
name_0 : String
description_0 : String
name_1 : String
description_1 : String
node_level : Int
node_type : Int
attr_jsonb : Jsonb
isaLevel : String
modelId : Int
valPrefix : String
standingData: Array
opcUALevel : Int
opcUANamespaceName : String
opcUAAddressPrefix : String
permissions : Int
…

## Slide 8: Vertex Placement Algorithm Overview
forEach vertex in pidVertices:
if (not group):
calculate cell area
store cell area
position current vertex:
get previous vertex position (x, y values)
apply positioning rules
set current vertex position
update value of previous x, y values
else if (group):
sum areas of contained cells
Simplification of edges (clear connection waypoints between various edges if any)
Jump
Constraint specification in the form of tags
Positioning logic in the form of rules (depending on tags)
Setting of parameters

## Slide 9: 1. Simplification of Edges Overview
forEach edge in pidEdges:
if (already simplified):
skip
else if ()
calculate cell area
store cell area
position current vertex:
get previous vertex position (x, y values)
apply positioning rules
set current vertex position
update value of previous x, y values
else if (group):
sum areas of contained cells

## Slide 10: Line Jumps Example:
Problem:
  Connections gehen vom Vertexmittelpunk zum Vertexmittelpunk
  Connections werden automatisch optimiert um Kreuzungen zu vermindern aber unmöglich alle zu vermeiden
  Dies führt zum Zusammenklappen verschiedene linen
  Unübersichtlich
Lösung:
  Line jumps
    Arc form
    radius 20pt

## Slide 11: 2. Constraint Specification Overview
Positioning Rules based on shape attributes:
Tags:

## Slide 12: 3. Vertex Placement Concept
Probleme:
  Inkonsistenzen in das Model (Instance Hierarchy) wie z.B. Gruppen die Gruppen aber auch Shapes enthalten.
  Führt zu Irreguläre Platzierung in die Mehrheit der Fälle  braucht zu viel Logik.
  Relative positionierung deswegen manchmal suboptimal, aber trotzdem die beste Alternative
  Viel Aufwand und wenig Fortschritt bei der Verbesserung des Algorithmus.
Lösungen (zum Teil):
  Specification of Constraints erlaubt Logik gezielt zu programmieren
  Constraints erlauben auch das progressive Enhancement
  Block packing algorithm ist eine optimale Lösung für P&ID Diagramme falls alle children Gruppen sind (rechteckige Blocks). Nicht aber für shapes.

## Slide 13: 3.1 Placement Logic Example:
Kleine Modifikationen zum vorherigen Logik
Sonst gleich

## Slide 14: 3.2 packBlocks() Overview
Binary tree block packing algorithm (for groups):
Sort blocks (clones) based on selected sortOrder option (none, width, height, area, maxSide)
Place first (root) block at (0, 0).
Place next block either right or bellow of previous (minimize area)
Repeat 3 until all blocks placed.
Update properties in original objects.
Sehr gute Ergebnisse für Blocks die nur Groupen sind (ohne Shapes)

## Slide 15: 3.2 packBlocks() Sort Order Options
by width
none (default)
by area
by height
by maxSide
Beispiel mit 4 Units in Brewery (block dimensions to scale)

## Slide 16: 3.2 Bugs in Boardlet Algorithmus Sort Order Options
Obwohl praktish identische Code, nicht gleiche Visu Output.
Testing Boardlet Sapient Boardlet

## Slide 17: Vertex Placement Concept
hp/2
wp/2
wn/2
(0, 0)
(-0.5,0.5)
(1, 1)
(0.5, 0.5)
Relative Positioning
vertex placement group placement group placement … (recursively)
Parent vertex
hn/2
spacing
Geometry between neighbouring children
y
(0, 0)
(x, y)
Hgmax (currently)
Wgmax (currently)
Optimal Fall (vor ein Paar Wochen):

## Slide 18: 3.3 Issues and Challenges Weekly Sprint 14
Stillstand beim vertexPlacement Algorithmus  fix bugs, then leave as is
  Alles wofür es eine bestimmte Logik dahinter gibt, wird schon entsprechend dieser Logik platziert.
  Nich viel mehr Logik um das Platzierungsalgorithmus in wenig Zeit noch zu verbessern.
  Verbesserungen machen manchmal andere Teilen von Code kaputt.
  Bugs im Algorithmus in Boardlet Script (nicht im Testing Boardlet).
  Vorteile:
    Konzentration auf Data-bindings (dynamisierung)
    Verteci schon ziemlich gut platziert und edges vereinfacht
    Verbesserungsmöglichkeiten direkt im draw.io (Drag&Drop)
  Nachteile:
    Platzierung ist das Endergebniss und alles was man am Ende sieht
    Arbeit und Aufwand die hinter die Visualisierung sieht man nicht
    Kann zu enttäuschenden Schlussfolgerungen bezüglich des Projekts führen
Bug wenn selectierte rootNode nicht AidaCruises  fix
Animations und Data Bindings
  Process Variables noch nicht im Datenbank vorhanden  Animationen nur als Konzept
  Model wird sowieso nur booleans enthalten  Konzept für andere Data Types oder nicht ?

## Slide 19: Vorläufige Inhaltsverzeichnis Bachelorarbeit
In Word…

## Slide 20: Project – Overview Overview of tasks: Week 10

## Slide 21
forEach vertex in pidVertices:
if (not group):
calculate cell area
store cell area
position current vertex:
get previous vertex position (x, y values)
apply positioning rules
set current vertex position
update value of previous x, y values
else if (group):
sum areas of contained cells